# SECTION 09 63 46 DIFINITI QUARTZ FLOORING

- - GENERAL

  - SUMMARY

    - Section Includes:

      - Quartz floor finishes.

      - Setting materials and accessories.

    - Related Sections:

      - Division 01: Administrative, procedural, and temporary work requirements.

      - Section [__ __ __ - _______] - Concrete substrate.

      - Section [__ __ __ - _______] - Wood substrate.

  - REFERENCES

    - American National Standards Institute (ANSI):

      - A108.5 - Installation of Ceramic Tile with Dry-Set Portland Cement Mortar or Latex Portland Cement Mortar.

      - A108.10 - Installation of Grout in Tilework.

      - A118.4 - Latex-Portland Cement Mortar.

      - A118.6 - Ceramic Tile Grouts.

    - ASTM International (ASTM):

      - C97 - Standard Test Methods for Absorption and Bulk Specific Gravity of Dimension Stone.

      - C99 - Standard Test Method for Modulus of Rupture of Dimension Stone.

      - C170 - Standard Test Method for Compressive Strength of Dimension Stone.

      - C241 - Standard Test Method for Abrasion Resistance of Stone Subjected to Foot Traffic.

      - C482 - Standard Test Method for Bond Strength of Ceramic Tile to Portland Cement.

      - C484 - Standard Test Method for Thermal Shock Resistance of Glazed Ceramic Tile.

      - C531 - Standard Test Method for Linear Shrinkage and Coefficient of Thermal Expansion of Chemical-Resistant Mortars, Grouts, Monolithic Surfacings, and Polymer Concretes.

      - C648 - Standard Test Method for Breaking Strength of Ceramic Tile.

      - C650 - Standard Test Method for Resistance of Ceramic Tile to Chemical Substances.

      - C672/C672M - Standard Test Method for Scaling Resistance of Concrete Surfaces Exposed to Deicing Chemicals.

      - C880 - Standard Test Method for Flexural Strength of Dimension Stone.

      - C1026 - Standard Test Method for Measuring the Resistance of Ceramic Tile to Freeze-Thaw Cycling.

      - C1028 - Standard Test Method for Determining the Static Coefficient of Friction of Ceramic Tile and Other Like Surfaces by the Horizontal Dynamometer Pull-Meter Method.

      - E84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

  - SUBMITTALS

    - Samples:

      - [4 x 4] [__ x __] inch quartz samples [in specified color.] [showing available colors.]

      - [3/8 x 3/8 x 3] [__ x __ x __] inch grout samples [in specified color.] [showing available colors.]

      - [3] [__] inch long joint sealer samples [in specified color.] [showing available colors.]

  - QUALITY ASSURANCE

    - Fabricator and Installer Qualifications: Minimum [2] [__] years [documented] experience in work of this Section.

    - Mockup:

      - Construct flooring mockup, [6] [__] feet wide x [6] [__] feet long.

      - Locate [where directed.] [____.]

      - Approved mockup may remain as part of the Work.

- - PRODUCTS

  - MANUFACTURERS

    - Contract Documents are based on products by Terrazzo & Marble Supply Co.

    - Substitutions: [Under provisions of Division 01.] [Not permitted.]

  - MATERIALS - QUARTZ

    - Quartz Sheet:

      - Product: DIFINITI.

      - Composition: Quartz aggregate, resin, and color pigments formed into flat slabs.

      - Color: [____.] [To be selected from manufacturer's full color range.]

      - Size: [____.] [To be selected from manufacturer's full format range.]

      - Physical characteristics:

        - Physical characteristics to meet all of the performance criteria of DIFINITI with regard to physical strength, chemical resistance, ease of maintenance and appearance.

  - MATERIALS - MORTAR

    - Standard Tile Formats: Latex-Portland Cement Mortar: 254 Platinum Multipurpose Thin-Set Mortar by Laticrete International, Inc. or Latex-Portland Cement Mortar: ANSI A118.4.

    - 24x24x3/8 Tile or 1 Dimension greater than 24”: 100% Solid Epoxy Adhesive: Latapoxy 300 Adhesive by Laticrete International, Inc. or 100% Solid Epoxy Adhesive: ANSI A118.3.

  - MATERIALS - GROUT

    - Grout:

      - 1500 Series [Sanded] or 1600 Series [Unsanded] Grout by Laticrete International, Inc or Polymer Fortified Cementitious Grout: ANSI A118.7

      - Color: [_____.] [To be selected from manufacturer's full color range.]

  - ACCESSORIES

    - Joint Sealer:

      - Latisil Tile and Stone Sealant by Laticrete International, Inc.

      - Color: [_____.] [To be selected from manufacturer's full color range.]

    - Crack Isolation Membrane

      - 170 Sound & Crack Isolation Mat by Laticrete International, Inc.

  - FABRICATION

    - Cut flooring accurately to required shapes and dimensions.

    - Cut flooring to fit at perimeter and around penetrations with maximum [1/4] [__] inch gaps.

- - EXECUTION

  - PREPARATION

    - Clean surfaces to receive flooring; remove loose and foreign matter than could interfere with adhesion.

    - Remove ridges and projections. Fill voids and depressions with patching compound compatible with setting materials.

    - Allowable Substrate Tolerances:

      - Maximum variation in substrate surface: 1/4 inch in 10 feet.

      - Maximum height of abrupt irregularities: 1/32 inch.

  - INSTALLATION

    - Install flooring in accordance with manufacturer's instructions.

    - Set flooring in thin set mortar bed in accordance with ANSI A 108.5.

    - Lay flooring to pattern furnished by Architect. Do not interrupt pattern through openings.

    - Install with [3/8] [__] inch joints.

    - Allow mortar to set for a minimum of 24 hours before grouting.

    - Grout joints in accordance with ANSI A108.10; finish smooth and flush.

    - Provide control joints at changes in plane, changes in substrate material, at joints between flooring and adjacent construction, over joints in substrate, and at maximum [__] feet on center. Fill with joint sealer; finish flush and smooth.

  - INSTALLATION TOLERANCES

    - Maximum variation from level and plumb: 1/4 inch in 10 feet, noncumulative.

    - Maximum variation in plane between adjacent pieces at joint: Plus or minus 1/16 inch.

    - Maximum variation in joint width: Plus or minus 1/16 inch.

  - CLEANING

    - Clean wall finishes in accordance with manufacturer's instructions.

# END OF SECTION